https://github.com/bdring/FluidNC
http://wiki.fluidnc.com/en/installation
https://github.com/bdring/6-Pack_CNC_Controller (no board schematics)
https://github.com/simon-jouet/ESP32Controller/blob/master/pdf/esp32controller.pdf (schematics esp32, I2S, to HC595)

https://randomnerdtutorials.com/esp32-pinout-reference-gpios/
GPIO	Input	Output	Notes
0	pulled up	OK	outputs PWM signal at boot / LOLIN button? / Joystick PB (Mode)
1	TX pin	OK	debug output at boot / Serial Comm Tx
2	OK	OK	connected to on-board LED? / UNUSED
3	OK	RX pin	HIGH at boot / Serial Comm Rx
4	OK	OK	TFT_RST
5	OK	OK	outputs PWM signal at boot / X_LIMIT
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high / SPINDLE_STEP (A_STEP_PIN)
13	OK	OK	SD_CS
14	OK	OK	outputs PWM signal at boot / SDI (I2S SR)
15	OK	OK	outputs PWM signal at boot / WCLK (I2S SR)
16	OK	OK	BCLK (I2S SR)
17	OK	OK	TFT_CS
18	OK	OK	TFT_SCK
19	OK	OK	TFT_MISO
21	OK	OK	TFT_DC
22	OK	OK	SPINDLE_OUTPUT_PIN (PWM)
23	OK	OK	TFT_MOSI
25	OK	OK	X_STEP
26	OK	OK	Z_STEP
27	OK	OK	Y_STEP
32	OK	OK	ADC1, ch4 T_CS
33	OK	OK	ADC1, ch5 Y_ANALOG (joystick)
34	OK		input only / Z_LIMIT ADC1, ch6
35	OK		input only / PROBE ADC1, ch7
36	OK		input only / X_ANALOG (joystick) ADC1, ch0
37	OK		input only / ENC1_Q1 ADC1, ch1 (Not on WROOM or NodeMCU)
38	OK		input only / ENC1_Q2 ADC1, ch2 (Not on WROOM or NodeMCU)
39	OK		input only / Y_LIMIT ADC1, ch3

NOTE THAT THE NODEMCU Needs a 2.2 uF capacitor between the RST/EN pin and ground in order to be able to flash from the IDE without pressing the BOOT button.