NOTE THAT THE NODEMCU Needs a 2.2 uF capacitor between the RST/EN pin and ground in order to be able to flash from the IDE without pressing the PGRM button.

GPIO	Input	Output	Notes
0	pulled up	OK	outputs PWM signal at boot / UNUSED
1	TX pin	OK	debug output at boot / UNUSED
2	OK	OK	connected to on-board LED? / UNUSED
3	OK	RX pin	HIGH at boot / UNUSED
4	OK	OK	TFT_RST
5	OK	OK	TFT_LED
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high / UNUSED
13	OK	OK	SD_CS
14	OK	OK	outputs PWM signal at boot / UNUSED
15	OK	OK	outputs PWM signal at boot / TFT_CS
16	OK	OK	UNUSED
17	OK	OK	UNUSED
18	OK	OK	TFT_SCLK
19	OK	OK	TFT_MISO
21	OK	OK	TFT_DC
22	OK	OK	TOUCH_CS
23	OK	OK	TFT_MOSI
25	OK	OK	Encoder Q1, INPUT_PULLUP (set by library)
26	OK	OK	Encoder Q2, INPUT_PULLUP (set by library)
27	OK	OK	Encoder Button, INPUT_PULLUP
32	OK	OK	PIR Sensor
33	OK	OK	DHT22 Data INPUT_PULLUP
34	OK		input only / UNUSED
35	OK		input only / UNUSED
36	OK		input only / ADC1_0 Light Level
37	OK		NOT PRESENT
38	OK		NOT PRESENT
39	OK		input only / UNUSED

https://www.youtube.com/watch?v=c0tMGlJVmkw&list=PLnwT_Zd4ZKYjpOVA3Mo5TGBYnDJL-yC3C&ab_channel=TheHookUp

pinMode(pin#, INPUT_PULLUP) incompatible pins: GPIO6-11, 34, 35, 36, 39
pinMode(pin#, INPUT_PULLDOWN) incompatible pins: GPIO0-3
Don’t use the following for outputs:
GPIO0, 1, 3, 5-11, 13-15, 34-39 Or, first check that ‘odd’ output during boot won’t cause problems in circuit.

## Product Description
Product Description:
AM312 body sensors modules:
A passive body based on the digital intelligent infrared technology, Automatic control products. High sensitivity, high reliability.
Widely used in various auto-sensing electrical equipment.
Features:
- Immunity enhancement, internal use of digital signal processing, direct high-low output.
- Repeatable trigger: the sensor output high after, the delay period, If there is human activity in its sensing range, the output will remain high until the people left after the delay, It becomes low (i.e. Sensor module detects the human body every activity will be automatically extended a period of time delay, and to the last activity time as the starting point of the delay time).
Specification:
1. Working voltage: DC 2.7-12V
2. Static power consumption: less than 0.1mA
3. Delay time: 2 seconds
4. The blocking time: 2 seconds
5. Trigger: can be repeated
6. Sensing range: ≤100 degree cone angle, 3-5 m; (required depending on the lens)
7. Working temperature: -20 - + 60 ℃
8. PCB Dimensions: 10mm x 8mm
9. Total size: Approx. 12mm x 25 mm
10. Module Lens: Small lens
Package Included:
5 x HC-SR312 AM312 Infrared Motion Sensor