NOTE THAT THE NODEMCU Needs a 2.2 uF capacitor between the RST/EN pin and ground in order to be able to flash from the IDE without pressing the PGRM button.

GPIO	Input	Output	Notes
0	pulled up	OK	outputs PWM signal at boot / UNUSED
1	TX pin	OK	debug output at boot / UNUSED
2	OK	OK	connected to on-board LED? / UNUSED
3	OK	RX pin	HIGH at boot / UNUSED
4	OK	OK	TFT_RST
5	OK	OK	outputs PWM signal at boot
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high / UNUSED
13	OK	OK	UNUSED
14	OK	OK	outputs PWM signal at boot / UNUSED
15	OK	OK	outputs PWM signal at boot / TFT_CS
16	OK	OK	UNUSED
17	OK	OK	UNUSED
18	OK	OK	TFT_SCLK
19	OK	OK	TFT_MISO
21	OK	OK	TFT_DC
22	OK	OK	TOUCH_CS
23	OK	OK	TFT_MOSI
25	OK	OK	Encoder Q1, INPUT_PULLUP (set by library)
26	OK	OK	Encoder Q2, INPUT_PULLUP (set by library)
27	OK	OK	Encoder Button, INPUT_PULLUP
32	OK	OK	PIR Sensor
33	OK	OK	DHT22 Data INPUT_PULLUP
34	OK		input only / UNUSED
35	OK		input only / UNUSED
36	OK		input only / ADC1_0 Light Level
37	OK		NOT PRESENT
38	OK		NOT PRESENT
39	OK		input only / UNUSED

https://www.youtube.com/watch?v=c0tMGlJVmkw&list=PLnwT_Zd4ZKYjpOVA3Mo5TGBYnDJL-yC3C&ab_channel=TheHookUp

pinMode(pin#, INPUT_PULLUP) incompatible pins: GPIO6-11, 34, 35, 36, 39
pinMode(pin#, INPUT_PULLDOWN) incompatible pins: GPIO0-3
Don’t use the following for outputs:
GPIO0, 1, 3, 5-11, 13-15, 34-39 Or, first check that ‘odd’ output during boot won’t cause problems in circuit.