GPIO	Input	Output	Notes
0	pulled up	OK	outputs PWM signal at boot / LOLIN button? / Encoder 1 PB
1	TX pin	OK	debug output at boot / UNUSED
2	OK	OK	connected to on-board LED? / Encoder 1 Q2
3	OK	RX pin	HIGH at boot / UNUSED
4	OK	OK	TFT_RST
5	OK	OK	outputs PWM signal at boot
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high / SPINDLE_STEP
13	OK	OK	SPINDLE_ENABLE
14	OK	OK	outputs PWM signal at boot / SPINDLE_DIRECTION
15	OK	OK	outputs PWM signal at boot / Encoder 1 Q1
16	OK	OK	Y_DIRECTION
17	OK	OK
18	OK	OK	TFT_SCLK
19	OK	OK	TFT_MISO
21	OK	OK	TFT_DC
22	OK	OK	TFT_CS
23	OK	OK	TFT_MOSI
25	OK	OK	X_STEP
26	OK	OK	X_ENABLE
27	OK	OK	X_DIRECTION
32	OK	OK	Y_STEP
33	OK	OK	Y_ENABLE
34	OK		input only / INPUT_1
35	OK		input only / INPUT_2
36	OK		input only / INPUT 3
37	OK		INPUT 4
38	OK		INPUT 5
39	OK		input only / INPUT 6